## Slide 1: Number Representation
Prepared by
Dr. Shahram Taheri

## Slide 2: Decimal Numbering System
We humans naturally use a particular numbering system

## Slide 3: Decimal Numbering System
For any nonnegative integer , its value is given by
  Here d0 is the least significant digit and dn is the most significant digit

## Slide 4: General Numbering System – Base X
Besides 10, we can use other bases as well
  In base X,
  Then, the base X representation of this number is defined as dndn-1…d2d1d0.
  The same number can have many representations on many bases. For 23 based 10, it is
    23ten
    10111two
    17sixteen, often written as 0x17.

## Slide 5: Commonly Used Bases
  Note that other bases are used as well including 12 and 60
Which one is natural to computers?
  Why?
Base | Common Name | Representation | Digits
10 | Decimal | 5023ten or 5023 | 0-9
2 | Binary | 1001110011111two | 0-1
8 | Octal | 11637eight | 0-7
16 | Hexadecimal | 139Fhex or 0x139F | 0-9, A-F

## Slide 6: Meaning of a Number Representation
When we specify a number, we need also to specify the base
  For example, 10 presents a different quantity in a different base

  There are 10 kinds of mathematicians. Those who can think binarily and those who can't... http://www.math.ualberta.ca/~runde/jokes.html

## Slide 8: Question
How many different numbers that can be represented by 4 bits?

## Slide 9: Question
How many different numbers that can be represented by 4 bits?
Always 16 (24), because there are this number of different combinations with 4 bits, regardless of the type of the number these 4 bits are representing.
Obviously, this also applies to other number of bits. With n bits, we can represent 2n different numbers. If the number is unsigned integer, it is from 0 to 2n-1.

## Slide 10: Conversion between Representations
Now we can represent a quantity in different number representations
  How can we convert a decimal number to binary?
  How can we then convert a binary number to a decimal one?

## Slide 11: Conversion From Binary to Decimal
Converting from binary to decimal. This conversion is based on the formula:
d = dn-12n-1 + dn-22n-2 +…+ d222 + d121 + d020
while remembering that the digits in the binary representation are the coefficients.
For example, given 101011two, in decimal, it is
25 + 23 + 21 + 20 = 43.

## Slide 12: Conversion From Decimal to Binary
Converting from decimal to binary:
  Repeatedly divide it by 2, until the quotient is 0.
  Write down the remainder, the last remainder first.
Example: 11ten is 1011two
Quotient | Remainder
5 | 1
2 | 1
1 | 0
0 | 1

## Slide 13: Conversion From Decimal to Binary
Why can a binary number be obtained by keeping on dividing it by 2, and why should the last remainder be the first bit?
  The decimal number can be represented by the summation of the powers of 2:
  d = dn-12n-1 + dn-22n-2 +…+ d222 + d121 + d020
    For example, 19 = 16 + 2 + 1 = 1 * 24 + 0 * 23 + 0 * 22 + 1 * 21 + 1 * 20.
  The binary representation is the binary coefficients.
    So 19ten in binary is 10011two.
  So the conversion is to find the coefficients. Easiest way to do so is to repeatedly divide it by 2.
    For example, 19 = 1 * 101 + 9 * 100. How do you get the 1 and 9? You divide 19 by 10 repeatedly until the quotient is 0, same as binary!

## Slide 14: Conversion between Base 16 and Base 2
Extremely easy.
  From base 2 to base 16: divide the digits in to groups of 4, then apply the table.
  From base 16 to base 2: replace every digit by a 4-bit string according to the table.
Because 16 is 2 to the power of 4.

## Slide 15: Addition in binary
39ten + 57ten = ?
How to do it in binary?

## Slide 16: Addition in Binary
First, convert the numbers to binary forms. We are using 8 bits.
  39ten -> 001001112
  57ten -> 001110012
Second, add them.
  00100111
  00111001
  01100000

## Slide 17: Addition in binary
The addition is bit by bit.
We will encounter at most 4 cases, where the leading bit of the result is the carry:
  0+0+0=00
  1+0+0=01
  1+1+0=10
  1+1+1=11

## Slide 18: Subtraction in Binary
13ten – 10ten = ?

## Slide 19: Subtraction in Binary
  1101
  1010
  0011
Do this digit by digit
  1. 1-0 -> 1
  2. 0-1, cannot do it because 0 is less than 1, so have to borrow, meaning looking to the left to find the first 1, in this case, it is the immediate left neighbor, so we borrow 1 from it, reducing it to 0, while we have 10 which is 2. 2-1 = 1, so we write 1 down as the current digit
  3. 0-0 -> 0, remember the borrow!
  4. 1-1 -> 0

## Slide 20: Subtraction in Binary
17ten – 10ten = ?

## Slide 21: Subtraction in Binary
  10001
  01010
  00111
Do this digit by digit
  1. 1-0 -> 1
  2. 0-1, cannot do it because 0 is less than 1, so have to borrow, meaning looking to the left to find the first 1. In this case, the immediate left neighbor, call it A, is also 0, so it will try to borrow from its left neighbor, call it B. B is 1, so A can borrow from B, reducing B to 0. A is now 10 (2 in decimal), but it has to lend us a 1, so it reduces to 1. We borrowed from A, we become 10 (2 in decimal), so we can handle the subtraction and we write 1 down as the current digit
  3. 1-0 -> 1, remember the borrow!
  4. 0-1, remember the borrow, cannot do it, but can borrow, so becomes 1.
  5. 0-0 -> 0, remember the borrow

## Slide 22: Subtraction in binary
Do this digit by digit.
No problem if
  0 - 0 = 0,
  1 - 0 = 1
  1 – 1 = 0.
When encounter 0 - 1, set the result to be 1 first, then borrow 1 from the next more significant bit, just as in decimal.
  Borrow means setting the borrowed bit to be 0 and the bits from the bit following the borrowed bit to the bit before the current bit to be 1.
  Think about, for example, subtracting 349 from 5003 (both based 10). The last digit is first set to be 4, and you will be basically subtracting 34 from 499 from now on.

## Slide 23: Signed Numbers
Two’s complement in n bits:
  The negative of a two’s complement is given by inverting each bit (0 to 1 or 1 to 0) and then adding 1, ignore any carry beyond n bits (take only the lower n bits).
If numbers are represented in n bits:
  the positive numbers are from 0000…01 to 0111…11,
  0 is all 0: 0000…00,
  the negative numbers are from 1000…00 to 1111…11.
The leading bit is called the “sign bit”: 0 means non-negative, 1 means nagative

## Slide 24: Signed numbers
What is (-57ten) in binary in 8 bits?
  00111001 (57ten in binary)
  11000110 (invert)
  11000111 (add 1)

## Slide 25: Question
What is the range of numbers represented by 2’s complement with 4 bits?
The answer is [-8,7].
This is because all numbers with leading bit being 1 are negative numbers. So we have 8 of them. Then 0 is all 0. Then seven positive numbers.

## Slide 26: Two’s Complement Representation
Type (C) | Number of bits | Range (decimal)
char | 8 | -128 to 127
short | 16 | -32768 to 32767
int | 32 | -2,147,483,648 to 2,147,483,647
long long | 64 | -9,223,372,036,854,775,808 to 9,223,372,036,854,775,807
n+1 bits (in general) | n+1 | -2n to 2n - 1

## Slide 27: Why use 2’s complement? (Not required)
If you think about it, x in 2’s complement with n bits is just 2n-x.
Consider 01101 +(– 00011) = 01101 – 00011 = 01010 (13-3=10 in decimal).
01101 – 00011 = 01101 + 100000 – 00011 – 100000
= 01101 + (100000 – 00011) – 100000
= 01101 + 11101 – 100000 = 101010 – 100000
= 01010
11101 is the 2’s complement of 00011.
Means that computer (the adder) does not have to be specifically redesigned for dealing with negative numbers, make life easier for the computer
The reason is, assume you are subtracting a with b , where 2^{n-1}>a>b>0. Note that a-b=a+2^{n}-b-2^{n}. But 2^{n}-b is the 2’s complement of b. So if represented in binary forms, a+2^{n}-b will be having a 1 bit in bit n and some thing in bit 0 to bit n-2 equal to a-b. Bit n-1 will be 0. So you take what is in bit 0 to bit n and it must be a-b.

## Slide 28: Subtraction with 2’s Complement
How about 39ten + (-57ten)?

## Slide 29: Subtraction with 2’s Complement
First, what is (-57ten) in binary in 8 bits?
  00111001 (57ten in binary)
  11000110 (invert)
  11000111 (add 1)
Second, add them.
  00100111
  11000111
  11101110

## Slide 30: Converting 2’s complement to decimal
  What is 11101110ten in decimal if it represents a two’s complement number?
  11101110 (original)
  11101101 (after minus 1)
  00010010 (after inversion)

## Slide 31: Two’s Complement Representation
Sign extension
  We often need to convert a number in n bits to a number represented with more than n bits
    From char to int for example
  This can be done by taking the most significant bit from the shorter one and replicating it to fill the new bits of the longer one
    Existing bits are simply copied

## Slide 32: Sign Extension Example
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | -3ten -3ten -3ten
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 
- How about unsigned numbers?

## Slide 33: Sign Extension Example: Unsigned
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | 252ten 252ten 252ten
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 

## Slide 34: Unsigned and Signed Numbers
Note that bit patterns themselves do not have inherent meaning
  We also need to know the type of the bit patterns
  For example, which of the following binary numbers is larger?

## Slide 35: Unsigned and Signed Numbers
Note that bit patterns themselves do not have inherent meaning
  We also need to know the type of the bit patterns
  For example, which one is larger?
    Unsigned numbers?
    Signed numbers?